## Slide 1
自然图像分割 Color Image Segmentation
数字图像处理 Digital Image Processing

## Slide 2
分水岭算法
Mean shift分割
Normalized cuts(Ncuts)分割
Ncuts分割改进算法
Graph cuts(GC) 优化
GC与交互式分割
Graph cut与变分模型
彩色图像分割及处理
Notes: 图像分割问题就是根据像素点之间的相似程度来确定不同的区域，从而分割图像，则定义相邻像素点之间的相似程度为边，相似程度越大，边的权值越大。而且很显而易见的一点是:不同区域之间的差异是非常大的，因此相邻区域之间连通的边的权值，一定都是较小的值(不同区域之间相似程度小，相邻边的权值就很小)。所以我们可以这样想: 找到了权值之和比较小的边集，就可能相当于找到了区域的边界。

## Slide 3
将节点间的关系采用带权图来表达
将图划分成两个部分或多个部分
图的划分

## Slide 4
如果将图像中的每个象素看作一个节点，每对节点均用一条边连接起来，边的权值反映这两个象素之间的相似性，那么我们就可以构建一个带权的无向图G=(V,E) 。利用象素的灰度值以及它们的空间位置，可以定义图G中连接两个节点u和v的边的权值
Segmentation=Graph Partition

## Slide 5: 图割(Graph Cuts)优化算法
Minimum Cut 容易产生孤立点
图的割集是与切割的边的数量及权值相关的
一个割集 cut(A, B) 将图分为独立的两个部分
A
B
图像 — 图
图像分割 — 图划分

## Slide 6
Disassociation Measures
Minimizing the cut will give a partition with the maximum disassociation.
However, this measure favors cutting to small sets of isolated nodes.

## Slide 7
Disassociation Measures
Normalized cut Ncut(A,B) measures similarity between two groups, normalized by the “volume” they occupy in the whole graph [Shi and Malik, 2000].
It is more appropriate to measure the disassociation between groups A and B.
minimize
A
B
A + B = V
Notes: 其中A,B均为点集，V为整个图像的总像素点集。ANB = cut(A,B)就是分割A，B两集合的割集的权值和，assoc(A,V)表示A中所有点与图中所有点 (即点集V) 相连的边的权值和。引入assoc这个函数后，就能比较好地避免分割出孤立点的情况，

## Slide 8: Graph-based Image Segmentation
V: graph nodes
E: edges connection nodes
G = {V,E}
Pixels
Pixel similarity
Slides from Jianbo Shi

## Slide 9: Graph terminology
Similarity matrix:

## Slide 10: Affinity matrix
Similarity of image pixels to selected pixel
Brighter means more similar
Reshape
N*M pixels
N*M pixels
M pixels
N pixels

## Slide 11: Graph terminology
Degree of node:
…
…

## Slide 12: Graph terminology
Volume of set:
总计140个点，假定1-95为集合A，96-140为集合B

## Slide 13: Graph terminology
Cuts in a graph:

## Slide 14: Graph terminology
Similarity matrix:
Degree of node:
Volume of set:
Graph cuts:

## Slide 15: Representation
Partition matrix X:
Pair-wise similarity matrix W:
Degree matrix D:
Laplacian matrix L:
segments
pixels

## Slide 16: Pixel similarity functions
Intensity
Texture
Distance

## Slide 17
Disassociation Measures
The solution to the problem
is given by the following eigen-system
minimize
For an image with N pixels, the matrix size is NxN.
Computational cost increases dramatically as the image size increases!

## Slide 18: Graph-based Image Segmentation
Image (I)
Graph Affinities
(W)
Intensity
Color
Edges
Texture

## Slide 19: Graph-based Image Segmentation
Image (I)
Graph Affinities
(W)
Intensity
Color
Edges
Texture

## Slide 20: Graph-based Image Segmentation
Image (I)
Eigenvector
X(W)
Graph Affinities
(W)
Intensity
Color
Edges
Texture

## Slide 21: Graph-based Image Segmentation
Image (I)
Eigenvector
X(W)
Discretization
Graph Affinities
(W)
Intensity
Color
Edges
Texture

## Slide 22
分水岭算法
Mean shift (MS) 分割
Normalized cuts(Ncuts)分割
Ncuts分割改进算法
Graph cuts(GC) 优化
GC与交互式分割
Graph cut与变分模型
彩色图像分割及处理

## Slide 23
Minimum Cut 容易产生孤立点
图的割集是与切割的边的数量及权值相关的
一个割集 cut(A, B) 将图分为独立的两个部分
A
B
图像 — 图
图像分割 — 图划分
改进1——基于Ncuts的阈值分割
Wenbing Tao, et.al, "Image Thresholding Using Graph Cuts", IEEE Transactions on Systems Man and Cybernetics Part A-Systems and Humans. 2008.

## Slide 24
Disassociation Measures
The solution to the problem
is given by the following eigen-system
minimize
For an image with N pixels, the matrix size is NxN.
Computational cost increases dramatically as the image size increases!

## Slide 25
正确的划分函数
有效的优化算法
计算Laplacian矩阵D-W的特征矢量
矩阵D、W和D-W的维数为图像中象素的个数
问题：维数太高，效率低下？
Jianbo Shi
最小化
NP难问题

## Slide 26: 基于图划分的阈值法基本原理
对每一个设定阈值T(0≦T≦255)计算Ncut(A, B)
最小的Ncut对应的阈值T为最佳阈值
计算高维权值矩阵耗时
权值矩阵太大无法存储
影响阈值方法的效率和实现

## Slide 27
Proposed Approach
Consider Vk, k = 0, …, 255 corresponds to the gray scale levels.

## Slide 28
Proposed Approach

## Slide 29
If Ncut(A,B)< Ncutmin, let Ncutmin = Ncut(A,B) and T=t. Let t=t+1.
Initialize t = 0, Ncutmin=2.
Compute the elements of matrix M (edge weights).
From matrix M, compute Ncut of the bisection V={A,B} corresponding to threshold t.
t<=255
Threshold the image using optimal threshold value T
No
Yes
Proposed Approach

## Slide 30
Advantages of the Proposed Approach
Low computational cost
Suited for real-time vision processing
Provide superior and robust image thresholding performance

## Slide 31
Pikaz
Kittler
Kapur
Yanowitz
Ramesh
Pal
Compared methods
Test images
Infrared object images
Standard test images
Experimental Results

## Slide 32
proposed
manual
histogram
Ncut
original
Experimental Results
Intruder – infrared image: 185 x 141
Other methods

## Slide 33
本文
理想
本文
理想
直方图
Ncut图
原始
原始
直方图
Ncut图

## Slide 34
本文
本文
原始
理想
理想
原始
直方图
Ncut图
直方图
Ncut图

## Slide 36
Experimental Results
Good results for standard test images
proposed
histogram
Ncut
original
Other methods

## Slide 37
Experimental Results
Good results for standard test images
proposed
histogram
Ncut
original
Other methods

## Slide 38
(f) r=4, dI=1000, dX=8
(g) r=4, dI=2000, dX=8
(h) r=4, dI=5000, dX=8
(i) r=4, dI=10000, dX=8
(j) r=4, dI=20000, dX=8
(d) r=16, dI=625, dX=32
(e) r=32, dI=625, dX=250
(a) r=2, dI=625, dX=4
(b) r=4, dI=625, dX=8
(c) r=8, dI=625, dX=16
Experimental Results
As r increases, the Ncut curve becomes smoother.
As dI increases, Ncut values increases.
In general, Ncut is insensitive to these parameters.
Tank image

## Slide 39
r=2, dI=1000, dX=4
r=4, dI=2000, dX=8
r=6, dI=3000, dX=10
r=8, dI=5000, dX=16
r=2, dI=4000, dX=4
r=4, dI=7000, dX=8
r=6, dI=13000, dX=10
r=8, dI=18000, dX=16
Experimental Results
Ship image
As dI increases to an extremely large value, the optimum value of T shifts from right to left.
This does not usually happen for typical values of dI (400 – 1000).

## Slide 40
Execution time vs. r.
Computational Complexity
Execution time vs. image size in the multiple of 128x128.